PLEASE CHECK TO MAKE SURE THAT THIS LIST IS CORRECT FOR YOUR NEEDS. YOU ARE SOLELY RESPONSIBLE AND LIABLE FOR WHAT YOU DO WITH THE INFORMATION CONTAINED IN THIS DOCUMENT.

Mnats Rev D Version 2.2 Parts List with links:

Date : 06/05/09

Control Click to go to links

RED = Signal Pre-amp part	GREEN = Signal Line Amp part		() = Rev D version 1 old part

BLUE SHADE  = Supplied by Hairball

ORANGE SHADE = Mouser

PINK SHADE = Supplied by Digikey

AQUA SHADE = refer to other supplier page

| # | mark | QTY | Value | Description | Designation | Catalog # |
| --- | --- | --- | --- | --- | --- | --- |
| FROM DIGIKEY - http://www.digikey.com/ |
| Ceramic Capacitors |
| 1 |  |  |  | 1 | 10pF | ceramic cap – monolithic | C11 5mm | P4837-ND Epcos Inc $0.27 US 100v 5% 2.5mm COG |
| 2 |  |  |  | 1 | 270pF | ceramic cap | C13 5mm | P4930-ND - N/A 881-0425 - Allied Electr. AVX $0.24 US each 100v 5% 2.5mm COG |
| 3 |  |  |  | 1 | 27pF | ceramic cap - monolithic | C2 | P4842-ND Epcos Inc $0.23 US 100v 5% 2.5mm COG |
| 4 |  |  |  | 2 | 200pF | Mica (ceramic) cap | C3,C6 | 490-3636-ND – just incase Muruta Elect. Nth Amer $0.37 US each 100v 5% 2.5mm 338-1063-ND - Cornell Dubilier Electronics (CDE) $1.45 US each 500v 5% 5.9mm |
| Electrolytic Capacitors |
| 5 |  |  |  | 1 | 6.8µF | electrolytic cap 35v (63v) -aluminum | C23 | 493-1925-ND Nichicon $0.32 US 63v 20% 2mm |
| 6 |  |  |  | 5 | 100µF | electrolytic cap 35v - radial | C12,C21,C28,C4,C5 | P10294-ND – just incase Panasonic ECG $0.38 US 35v 20% 3.5mm 539-SEK35V100 – Mallory $0.72 US each 35v 20% 3.5mm |
| 7 |  |  |  | 1 | 47µF | electrolytic cap 35v - radial | C18 | P11232-ND – Panasonic ECG $0.34 US 35v 20% 2.5mm |
| 8 |  |  |  | 1 | 2200µF | electrolytic cap 35v - radial | C24 | P5556-ND – Panasonic ECG $1.71 US 35v 20% 7.5mm |
| 9 |  |  |  | 2 | 2200µF | electrolytic cap 50v | C25,C26 | P5576-ND – Panasonic ECG $1.74 US 50v 20% 7.5mm |
| 10 |  |  |  | 3 | 1µF | Elec or film (electrolytic cap) - 50v | C7,C10,C17 | P10312-ND – Panasonic ECG $0.27 US 50v 20% 2mm |
| FROM MOUSER - http://au.mouser.com |
| Tantalum Caps |
| 11 |  |  |  | 2 | 6.8µF | tantalum capacitor – 35v | C19,C20 | 80-T350F685K035AT Kemet $0.67 US 35v 10% |
| Film Caps |
| 12 |  |  |  | 1 | 1µF | Ceramic Film (Wima MKS2-series 63v) | C1 | 505-MKS21.0/63/5 – Wima $1.10 US 63v 5% 5mm |
| 13 |  |  |  | 1 | .033µF | Cap film (MKP2-series 100v) | C14 | 505-MKP20.033/100/5 – Wima $0.46US 100v 5% 3mm |
| 14 |  |  |  | 1 | 4.7nF = 0.0047uf | Cap film (MKP2-series 100v) | C15 | 505-MKP24700/100/5 – Wima $0.27 US 100v 5% 5mm |
| 15 |  |  |  | 2 | .22µF | Cap film (MKP2-series 100v) | C9, C22 | 505-MKP20.22/100/5 – Wima $1.02 US 100v 5% 5mm |
| 16 |  |  |  | 1 | .22µF | MKS2-series 50v (more narrow) | C22 | 505-MKS2.22/50/10 |
| 17 |  |  |  | 1 | 22nF = 0.022uf | Cap film (MKP2-series 100v) on ratio board | C27 | 505-MKP20.022/100/5 – Wima $0.44 US 100v 5% 5mm |
| 18 |  |  |  | 1 | .15µF | Cap Film(MKP2-series 100v) | C8 | 505-MKP20.15/100/5 – Wima $0.87 US 100v 5% 5mm |
| Diodes |
| 19 |  |  |  | 1 | 1N914 | Diode (Fairchild small signal) | CR1 | 512-1N914A – Fairchild Semiconductor $0.02 US 100v |
| 20 |  |  |  | 1 | 1N4740A | zener (Vishay 10v Zener) | CR6 | 78-1N4740A – Vishay Semiconductors $0.04 US 10v |
| 21 |  |  |  | 2 | FDH333 | Diode high conductance (Fairchild low-leakage) *DO NOT SUBSTITUTE | CR2,CR3 | 512-FDH333 - included with mnats boards – Fairchild Semiconductors $0.10 US 150v |
| 22 |  |  |  | 4 | 1N4003 (1N4004) | Rectifier (Vishay Rectifier) | CR10,CR7,CR8,CR9 | 625-1N4004-E3 Vishay semiconductors $0.04 US 400v 45A – just incase. 512-1N4003 – Fairchild Semiconductors $0.07 US 200v 30A |
| Transistors |
| 23 |  |  |  | 2 | 2N5457 | Transistor fet (Fairchild N-channel FET) - matched | Q1,Q11 | 512-2N5457 |
| 24 |  |  |  | 7(14) | 2N3708 | Transistor bipolar (NPN Transistor) | Q5,Q7,Q8,Q9,Q10,Q12,Q13 Q7-Q10 All HFE > 250; Q12-Q13 matched by 10% Test HFE using a Multimeter. There should be a setting in there. | 610-2N3708 – Central Semiconductors $0.30 US 30v 45 @ 1mA @ 5v - 610-2N3707 – Central Semiconductor $0.38 US 30v 100 @ 100uA @ 5v 610-2N5088 – Central Semiconductor $0.37 US 30v 300 @ 100uA @ 5V |
| 25 |  |  |  | 4 | 2N3391 | Transistor bipolar (NPN Transistor) | Q2,Q3,Q4,Q14 | 610-2N3391A – Central Semiconductor $0.34 US 25v 250 @ 2 mA @ 4.5 V |
| 26 |  |  |  | 1 | 2N3053 | Transistor bipolar (Transistor medium pwr) | Q6 *use to-5 heatsink | 610-2N3053 – Central semiconductor $0.76 US 40v 25 @ 150 mA @ 2.5 V |
| Trimpots, hardware, misc. |
| 27 |  |  |  | 4 | 2k var | Trimmer potentiometer (trim pot) | R59, R71, R75, R44 * multiturn | 72-T93YB-2K – Vishay/Sfernice $1.44 US 2Kohm 10% |
| 27b |  |  |  | 1 | 1k | Trimmer potentiometer | R44 * tracking adjustment | 72-T93XA-1K – Vishay/Sernice $1.51 US 1 KOhms 10% |
| 28 |  |  |  | 1 | 100Ω = 100R | Trimmer potentiometer (trim pot) | R86 * distortion trim | 72-T93YA-100 – Vishay/Sfernice $1.44 US Multiturn 72-T93YB-100 – Vishay/Sfernice $1.44 US Multiturn Trimmer 3/8’ 100 Ohms 10% |
| 29 |  |  |  | 1 | 4-pole (3-pos) | Lorlin rotary switch | S2 * for knob ratio and meter | 10WA347 |
| 30 |  |  |  | 1 | 2-pole (6-pos) | Lorlin rotary switch | S4 * for knob ratio and meter | 10WA345 |
| 31 |  |  |  | 1 | 7824 | voltage regulator | VR1 * use to-220 heatsink | 512-MC7824AECT – Fairchild Semiconductor $0.75 US 24v 2% Positive |
| 32 |  |  |  | 1 | TO-5 heatsink | for output transistor | for Q6 | 532-578305B00 – Aavid Thermalloy $0.53 TO-5 19.05 mm L x 21.082 mm W x 10.033 mm H |
| 33 |  |  |  | 1 | TO-220 heatsink | for voltage regulator | for VR1 | 290-1AB – Wakefield $0.38 US 1 in L x 0.5 in W x 1.18 in H 532-507002B00 – Aavid Thermalloy $0.25 US 17.78 mm L x 44.45 mm W x 9.652 mm H 532-529802B25G – Aavid Thermalloy $1.38 US 41.91 mm L x 25.4 mm W x 38.1 mm H – just incase |
| 34 |  |  |  | 1 | Molex 2-position | terminal blocks | input | 538-39880-0302 – Molex $0.46 US |
| 35 |  |  |  | 7 | Molex 3-position | terminal blocks | various | 538-39880-0303 – Molex $0.79 US |
| 36 |  |  |  | 16 | pcb mount | matrix pins | rotary and meter board only get these for particular rotary PCB boards for GR and Ratio. | 538-02-06-8103 – Molex $0.13 US Male Solder tail People have complaint about these parts above being incorrect. They should look like these I think: HP1250 - 0.9mm PCB Pins - Pk.50 $4.50 AUD |
| 36b |  |  |  | 2 | 6 pin straight lock header | 6 Pin 0.1 Straight Locking Header - 2.54 pitch – Single | Use with 37b. Solders to Hairball Ratio and GR boards. Please confirm with how you set up your Ratio and GR switching for your build. Are you using Rotary switches or Push button banks? | Australian link HM3416 - 6 Pin 0.1 Straight Locking Header - 2.54 pitch - Single $0.60 AUD |
| 37 |  |  |  | 16 | wire end | female connectors | for matrix pins - 36 only get these for particular rotary PCB boards for GR and Ratio. | 538-02-06-1103 Molex $0.09 US Female Crimp terminals People have complaint about these parts above being incorrect. They should look like these I think: HP1260 - PC Pin Sockets to Suit PCB Pins - Pk.25 $5.50 AUD |
| 37b |  |  |  | 2 | 6 Pin 0.1 Header with Crimp Pins | 6 Pin 0.1 Header with Crimp Pins - 2.54 pitch | Connects to 36b for Hairball Ratio and GR boards. Please confirm with how you set up your Ratio and GR switching for your build. Are you using Rotary switches or Push button banks? | HM3406 - 6 Pin 0.1 Header with Crimp Pins - 2.54 pitch $0.75 AUD |
| Resistors |
| 38 |  |  |  | 4 | 10k | Resistor 1/4w | R10, R31, R35, R66 | 271-10k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 39 |  |  |  | 1 | 82 | Resistor 1/4w | R11 | 271-82-RC – Xicon $0.13 US 500v 0.25w 1% |
| 40 |  |  |  | 1 | 1.8k | Resistor 1/4w | R12 | 271-1.8k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 41 |  |  |  | 2 | 1M | Resistor 1/4w | R13, R36 | 271-1.0M-RC – Xicon $0.13 US 500v 0.25w 1% |
| 42 |  |  |  | 1 | 22k | Resistor 1/4w | R14 | 271-22k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 43 |  |  |  | 2 | 6.8K (7.5k) | Resistor 1/4w | R15 included in #45 | 271-7.5k-RC |
| 44 |  |  |  | 1 | 3.6k | Resistor 1/4w | R16 * on meter board | 271-3.6k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 45 |  |  |  | 2 (1) | 6.8k | Resistor 1/4w | R15, R17 | 271-6.8k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 46 |  |  |  | 3 | 180 | Resistor 1/4w | R18, R50, R84 | 271-180-RC – Xicon $0.13 US 500v 0.25w 1% |
| 47 |  |  |  | 2 | 68k | Resistor 1/4w | R19, R26 * R19 Ratio Board | 271-68k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 48 |  |  |  | 3 | 56k | Resistor 1/4w | R20,R21,R78 * R78 Ratio Board | 271-56k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 49 |  |  |  | 5 | 47k | Resistor 1/4w | R22,R38,R46,R52,R53 | 271-47k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 50 |  |  |  | 3 | 2.7M | Resistor 1/4w | R24, R25, R74 | 291-2.7M-RC – Xicon carbon film $0.10 US 500v 0.25w 5% |
| 51 |  |  |  | 6 | 1.5k | Resistor 1/4w | R27, R63, R64, R68, R69, R72 * R63 Ratio Board | 271-1.5k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 52 |  |  |  | 2 | 27k | Resistor 1/4w | R28,R5 | 271-27k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 53 |  |  |  | 1 | 1.2M | Resistor 1/4w | R29 | 291-1.2M-RC – Xicon Carbon Film $0.10 US 250v 5% 0.25w |
| 54 |  |  |  | 1 | 150k | Resistor 1/4w | R30 | 271-150k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 55 |  |  |  | 1 | 39 = 39R | Resistor 1/4w | R32 | 271-39-RC – Xicon $0.13 US 500v 0.25w 1% |
| 56 |  |  |  | 2 | 560 = 560R | Resistor 1/4w | R33, R62 | 271-560-RC – Xicon $0.13 US 500v 0.25w 1% |
| 57 |  |  |  | 3 | 8.2k | Resistor 1/4w | R34, R76, R77 *R77 optional resistor if using push button | 271-8.2k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 58 |  |  |  | 1 | 470k | Resistor 1/4w | R37 | 271-470k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 59 |  |  |  | 3 | 4.7k | Resistor 1/4w | R39,R51,R70 | 271-4.7k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 60 |  |  |  | 2 | 270 = 270R | Resistor 1/4w | R4, R41 | 271-270-RC – Xicon $0.13 US 500v 0.25w 1% |
| 61 |  |  |  | 2 | 2.4k | Resistor 1/4w | R40,R49 | 271-2.4k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 62 |  |  |  | 1 | 182k | Resistor 1/4w | R42 | 271-182k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 63 |  |  |  | 1 | 38.3k | Resistor 1/4w | R43 | 271-38.3k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 64 |  |  |  | 3 | 1k | Resistor 1/4w | R8,R81,R82 | 271-1k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 65 |  |  |  | 1 | 10M | Resistor 1/4w | R45 * ratio board | 291-10M-RC – Xicon Carbon Film $0.10 US 250v 0.25w 5% |
| 66 |  |  |  | 1 | 44.2k | Resistor 1/4w | R47 | 271-44.2k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 67 |  |  |  | 1 | 7.68k | Resistor 1/4w | R48 | 271-7.68k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 68 |  |  |  | 2 | 470 | Resistor 1/4w | R54, R61 * ratio board | 271-470-RC – Xicon $0.13 US 500v 0.25w 1% |
| 69 |  |  |  | 1 | 270k | Resistor 1/4w | R57 | 271-270k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 70 |  |  |  | 2 | 150 | Resistor 1/4w | R58, R85 | 271-150-RC – Xicon $0.13 US 500v 0.25w 1% |
| 71 |  |  |  | 2 | 2.2M | Resistor 1/4w | R6, R7 | 271-2.2M-RC – Xicon $0.13 US 500v 0.25w 1% |
| 72 |  |  |  | 2 | 3.9k | Resistor 1/4w | R60,R67 | 271-3.9k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 73 |  |  |  | 1 | 2.2k | Resistor 1/4w | R64 changed and added to 51 | 271-2.2k-RC |
| 74 |  |  |  | 1 | 3.9M | Resistor 1/4w | R65 * ratio board | 291-3.9M-RC – Xicon Carbon Film $0.10 US 250v 0.25w 5% |
| 75 |  |  |  | 1 | 680 = 680R | Resistor 1/4w | R73 | 271-680-RC – Xicon $0.13 US 500v 0.25w 1% |
| 76 |  |  |  | 1 | 15k | Resistor 1/4w | R79 | 271-15k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 77 |  |  |  | 1 | 220 = 220R | Resistor 1/4w | R89 | 271-220-RC – Xicon $0.13 US 500v 0.25w 1% |
| 78 |  |  |  | 1 | 560k | Resistor 1/4w | R9 | 271-560k-RC – Xicon $0.13 US 500v 0.25w 1% |
| 79 |  |  |  | 1 | 1.1k | Resistor 1 watt (2 watt) | R87 * mount above board (on top) | 282-1.1K-RC – Xicon Metal Oxide Power Resistor $0.19 2w 5% 594-5073NW1K100J – Vishay Metal Film $0.16 US 350v 1w 5% - just incase 261-1.1K-RC – Xicon Metal Oxide Power Resistor $0.13 1w 5% |
| 79b |  |  |  | 1 | 220R | Resistor 5 watt | VU lamp, to downgrade from 35v to 11.78v for 12v lamp | 286-220-RC – Xicon Metal Oxide Power Resistor $0.49 US 5w |
| Potentiometers |
| 80 |  |  |  | 1 | 25k (linear taper) | Potentiometer | R55 * attack pot with or without switch | 31VA403-F – Alpha Panel Mount Potentiometer $1.40 US 20% Solder Lug NO SWITCH 315-2415F-25K – Alpha 24mm Carbon Potentiometers Linear SPDT 25K Screwdrvr Solder Lug $3.15 US WITH SWITCH |
| 81 |  |  |  | 1 | 5M (4.7M linear taper) | Potentiometer | R56 * release pot | 31VA605-F – Alpha Panel Mount Potentiometer $1.40 US 20% Solder Lug |
| 82 |  |  |  | 1 | 250k log taper | Potentiometer (output pot) | R23 * audio taper | 31VJ503-F – Alpha Panel Mount Potentiometer $1.40 US 20% Solder Lug |
| Optional Additional Resistor |
| 83 |  |  |  | 1 | 8.2k | Optional Resistor if using pushbuttons | R77 *added to 57 and changed from 1 watt to ¼ watt power. | 261-8.2K-RC |
| ITEMS FROM OTHER SUPPLIERS - http://www.hairballaudio.com/shop/ |
| 84 |  |  |  | 1 | 2x22v or 2x25v | toroidal power transformer | Avel Lindburg | Y236105 or Y236106 |
| 85 |  |  |  | 1 | dc gapped, tertiary feedback winding | output transformer | EA-5002 (Cinemag) | CM-96731 |
| 86 |  |  |  | 1 | 500Ω / 200Ω | input transformer | C-3837-1 (UTC) | O-12, A-20, and A-21 are acceptable substitutes |
| 87 |  |  |  | 1 | 600Ω | T-pad or H-pad | Clarostat, Daven, Mallory, etc. | NOS |
| 88 |  |  |  | 1 | Sifam (new) or used/NOS | VU Meter | HB-8037 (true VU meter from Jewel, Dixson, Hoyt, Pulsar, Weston, etc.) | Sifam AL-29WF or NOS (also: Sifam 12v Illumination Kit) |
| 89 |  |  |  | 1 | 28 Pin Header Terminal Strip | 28 Pin Header Terminal Strip | Used for the R44 trimmer pot to be in circuit, short or normal. Use only 3 pins of it. Need the appropriate jumper link part that’s used for Hard Drives.Grab an old HD and it should have one. | HM3211 - 28 Pin Header Terminal Strip $0.85 AUD |

There are also other parts to consider like:

- 22 gauge hook up wire

http://www.jaycar.com.au/productView.asp?ID=WH3025&keywords=hook+up+wire&form=KEYWORD

- 2 core shielded wire

http://www.jaycar.com.au/productView.asp?ID=WB1504&keywords=2+core+cable&form=KEYWORD

- Microphone 2 core shielded wire

http://www.jaycar.com.au/productView.asp?ID=WB1530&keywords=2+core+cable&form=KEYWORD

- Single core shielded wire

- Single core audio cable

http://www.jaycar.com.au/productView.asp?ID=WB1508&keywords=core+cable&form=KEYWORD

- Power cable wiring (I used any standard power cable wire like from a kettle and strip them and use those wires for my power wiring)

-  Phone Type Crimp Lugs for the VU meters

http://www.jaycar.com.au/productView.asp?ID=PT4520&keywords=crimp&form=KEYWORD

- Fully Insulated Female Spade for the IEC power socket, Power transformer, etc.

http://www.jaycar.com.au/productView.asp?ID=PT4525&keywords=crimp&form=KEYWORD

- Eye terminals or similar for grounding wire to case

http://www.jaycar.com.au/productView.asp?ID=PT4514&keywords=crimp&form=KEYWORD

- Cable clamps or mounts to neaten up wiring.

http://www.jaycar.com.au/productView.asp?ID=HP0756&keywords=pcb+mount&form=KEYWORD

http://www.jaycar.com.au/productView.asp?ID=HP0782&keywords=pcb+mount&form=KEYWORD

- Spacers for PCB board mounting into case.

http://www.jaycar.com.au/productView.asp?ID=HP0900&keywords=pcb+mount&form=KEYWORD

- Male and Female XLR sockets and maybe a TRS/TS socket if you are adding stereo linking.

- Fused Male IEC panel mount.

- Nuts, Bolts, Washers, Lock washers, Spring Washers, etc. to mount IEC power socket, XLR sockets, PCB mounts, Transformers, etc.

*** NOTE: From my experience, Nuts, Washers, Lock washers, Spring washers and Bolts are very expensive if you buy from hardware stores or electronic stores. I suggest locating a Nut and Bolt Supplier or manufacturer in your area like my example below. It is ridiculous at how much electronics and hardware stores sell these items for at small quantities!!!!

Economy Bolt Company Pty Ltd

Cnr Hammond & Villas Rd Dandenong South VIC 3175 - get directions 
ph: (03) 9768 2599

Look thru the yellow pages or the business directory in your area to find a suitable nuts & bolts resource.